## Slide 1: GPS Navigation System
ET 494 - Spring 2018
By: Dylan Landry, Jordan Melancon, & Miguel Rodriguez
Advisor: Dr. Koutsougeras
Professor: Dr. Koutsougeras

## Slide 2: Introduction
Global Positioning System
  Orbiting satellites transmit unique signals to GPS device
  Device decodes signals and computes precise location
Current technology has integrated GPS into many motorized systems

## Slide 3: Project Goals
The overall goal is to implement an applicable GPS navigation system. With minor hardware changes, this model can be applied to various motorized systems.
Ex: RC Car, RC Boat, Push Lawn Mower

## Slide 4: Initial Work Plan
Figure out what parts we want to use
Learn how GPS gets coordinates
Design an interface to save and send coordinates
Learn how to link our interface and GPS with Bluetooth
Rewire and take control of RC car motors

## Slide 5
Item | Cost
HC-06 Bluetooth Module | $8.99
Adafruit Ultimate GPS Breakout | $39.95
GMAXT RC Car | $70.99
Arduino Mega ADK | Free (normally $47.30)
5V GS-T DPDT Relay | $2.15 x 4
4N25 Optocoupler | $0.48 x 4
HC-SR04 Ultrasonic Sensor | $3.95
Total (before taxes + shipping) | $134.40

## Slide 6: Mobile App
MIT App Inventor 2
Block Code
Simple Design
Real Time Testing

## Slide 7: Mobile App
Setup
Interfacing with Bluetooth
Problems

## Slide 8: GPS Module
Adafruit Ultimate GPS Breakout
Built-in antenna (room for external antenna)
Accuracy within 3 meters (9.8 feet)
Adafruit GPS Library for Arduino1

## Slide 9: Bluetooth Module
HC - 06 Model
Range of 10 meters (32.8 feet)
Works on 9600 baud for Arduino
Interfacing with Arduino and GPS module
Bluetooth Parsing

## Slide 10: RC Car Motor Control
Motor Voltage Spike off
Motor control protective Circuit
  Typical Optocoupler:

## Slide 11: RC Car Motor Control cont.
Relays (5v dc reed SPST )
Bi-directional Motor Control Circuit
  Combination of optocoupler (4N25) and relays (5v GS-T DPDT)
Hardware setup -- ready to ensemble the system.
  Bypass factory Controllers.
  RC car made easy to access wiring for ensembling and future modification.

## Slide 12
Circuit Control Schematic

## Slide 13: Fine Tuning & Troubleshooting Motor Control
Voltage spikes caused component failure
Replacement of potentiometer reading
Tuning and testing the power modulation for speed control
Limited space for the circuit and other components

## Slide 14: Improving GPS
Trimmed down full GPS code
All calculations run in its own function
Addition of heading angle

## Slide 15: Logic Flowchart

## Slide 16: Navigation Calculations
Distance Calculation
  Haversine Formula
  Why is this needed?
Angle calculation
  Why is this needed?

## Slide 17: Obstacle Detection and Avoidance
HC-SR04 Ultrasonic Sensor
Moving Average
Avoidance system

## Slide 18: Final Build

## Slide 19: Overall Accomplishments
Design an app in which you can input your desired location to the GPS system
  We added GPS calculations such as distance and angle equations so that we can find our current distance and degree angle from our target location.
Setup the GPS module to output coordinates to and from the app
  Improved our sending and receiving of GPS coordinates from the app to the Arduino.
Be able to direct the RC vehicle the direction it needs to go based on the coordinates
  RC car also now has full control for forward, backward, right, and left.
  Completely implement our GPS system with the motor control.

## Slide 20: Sources
HC-06 Bluetooth Module:
https://www.amazon.com/Pass-Through-Communication-Compatible-Atomic-Market/dp/B00TNOO438
Breakout GPS Module:
https://www.adafruit.com/product/746?gclid=EAIaIQobChMI-PvqyNzi1wIVgR2BCh2GjQb4EAAYASAAEgKHfPD_BwE
GMAXT RC Car:
https://www.amazon.com/GMAXT-Remote-Control-off-road-Vehicles/dp/B073Z29RW9
Arduino Mega ADK:
https://store.arduino.cc/usa/arduino-mega-adk-rev3
5v GS- T DPDT Relay
https://www.rapidonline.com/good-sky-gs-sh-205t-5v-dpdt-subminiature-relay-60-4754
4N25 Optocoupler:
http://www.bristolwatch.com/ele/opto_isolated.htm
5v DC Reed SPST Relay
https://www.radioshack.com/products/spst1a-5vreed-rly
HC-SR04 Ultrasonic Sensor
https://www.sparkfun.com/products/13959

## Slide 21: References
1.) Arduino Wiring | Adafruit Ultimate GPS | Adafruit Learning System. (n.d.). Retrieved from
https://learn.adafruit.com/adafruit-ultimate-gps/arduino-wiring
2.) haversine-geolocation. (n.d.). Retrieved from
https://www.npmjs.com/package/haversine-geolocation 3.) Material Design. (n.d.). Retrieved from
https://material.io/